## Slide 1
Autonomous Air transportation
Using Vision Navigation
Supervised by: Asst. Prof. Osama Saaid
Introduction
AC Design
Autopilot
Computer Vision
Implementation
Flight test

## Slide 2: Mission
Autonomous air transportation using vision navigation
AC Design

## Slide 3: Why Quad-plane?
POC | Fixed-wing | Multi-copter | Quad-plane
Vertical takeoff and landing | No | Yes | Yes
Comfortable | Yes | No | Yes
Power consumption | Low | High | Low
Cruise speed | High | Low | High
Endurance | Long | Short | Long
Range | Long | Short | Long
AC Design

## Slide 4: Scaled model
Why?!
A 1/100 scaled model based on payload
80 kg passenger
20 kg luggage
20 kg navigation equipment
1.2 kg
A full scaled model
A 1/100 scaled model
1/100
AC Design

## Slide 5: Mission
Payload
Payload | total estimated weight (gm)
Passenger | 200
Chair | 100
electronics | 300
Rasperry pi 2 | 42
XPAL power supply | 517
Pixhawk | 38
Jetson Kit | 431
RP Lidar A1 | 190
ZED camera | 159
Total mass | 2000 gm
AC Design

## Slide 6: Payload optimization
Payload | weight (gm) | Optimized payload | Optimized weight
Passenger | 200 | Passenger | 200
Chair | 123 | Chair | 123
electronics | 300 | Electronics | 300
Rasperry pi 2 | 42 | - | 0
XPAL power supply | 517 | - | 0
Pixhawk | 38 | Pixhawk | 38
Jetson Kit | 431 | Mini Jetson Kit | 150
RP Lidar A1 | 190 | - | 0
ZED camera | 159 | ZED camera | 159
Total mass | 2000 gm | Total mass | 970 gm
AC Design

## Slide 7: Sizing
Main payload
New Payload
VTOL Propulsion system
Fixed-wing
sizing
MTOM
Mission
AC Design

## Slide 8: Sizing
As a multi-copter
As a fixed-wing
component | Mass of a piece | No of pieces | Total mass
VTOL motors | 71 | 4 | 284
VTOL propellers | 19 | 4 | 76
VTOL ESC | 25 | 4 | 100
Total mass | - | - | 460 gm

## Slide 9: Propulsion system selection
Autonomous air transportation using vision navigation
AC Design

## Slide 10: VTOL
Motors
  KDE2315XF-2050-BRUSHLESS MOTOR

## Slide 11: Cruise
For a Minimum level of power for decent performance models
  KDE2814XF-775-BRUSHLESS MOTOR

## Slide 12: Battery
Using a MATlab code based on the following assumptions:
  Propulsion system power requirements
  20 mins endurance
  VTOL motors used in takeoff, landing and control
  Cruise motor is used during cruise only
  Landing and takeoff endurance equal 2 mins each
Needed battery capacity is 14600 mAh
Available batteries in the world market is maximum of 10500 mAh
AC Design

## Slide 13: Due to limited resources
Autonomous air transportation using vision navigation
AC Design

## Slide 14: Propulsion system limitations
Takeoff weight
  1st set of motors
  2nd set of motors
5200 mAh battery
  Endurance 6 mins
  Range
AC Design

## Slide 15: Mechanical design
Autonomous air transportation using vision navigation
AC Design

## Slide 16: Machining constraints
Available machines
  Laser cutter
    Only cuts foam and wood sheets with maximum size of (80*50 cm)
  CNC foam forming
    Forms wings form foam using hot wire with moderate accuracy
  3D printer (20*10*20 cm)
AC Design

## Slide 17: Building a 3D mechanical model
Why SolidWorks
Steps to build a mechanical design
  Define components geometry and mass properties
  Define CG location resulted from XFLR5 analysis
  Define geometric dimensions resulted from XFLR5 analysis
  Define components position constraints (cameras, lidars and PIX4)
  Take wiring clearance inconsideration
AC Design

## Slide 18: Payload
AC Design

## Slide 19: Propulsion system
AC Design

## Slide 20: Design iterations
1st iteration
AC Design

## Slide 21: Design iterations
2nd iteration
AC Design

## Slide 22: Design iterations
3rd iteration
AC Design

## Slide 23: Design iterations
4th iteration
AC Design

## Slide 24: Design iterations
6th iteration
AC Design

## Slide 25: Design iterations
7th iteration
AC Design

## Slide 26: Design iterations
8th iteration
AC Design

## Slide 27: Design iterations
9th iteration
AC Design

## Slide 28: Design iterations
10th iteration
AC Design

## Slide 29: Design iterations
11th iteration
AC Design